JM612-V6 Explosion Proof Robot Speed Dome

The body of JM612-V6 Robot Series is machined from 8mm~22mm thick 6063# Aluminum Alloy or 316#Stainless Steel. They are integrated with Sony 530TVL Day/Night Cameras and 360 degree continues Pan/Tilt rotation. The solid dome body are designed and proved to be explosion proof and to be resistant to impact from the destructiveness of stones, bricks, normal explosion and even short gun bullets.

The height of JM612-V6 Series dome body is lower than the JM612-V8 Series that is used in loading vehicles. The housing of the JM612-V6 Series is more spacious than other modules.

The JM612-V6 Series are also integrated with the special 5 Proofs design. That is: Bullet proof, Vandal proof, Water proof, Corrosion proof and Explosion proof. Because of its explosion proof features it is very popular in “Hazardous Areas” or an “Explosive Atmosphere” and in the likely/related areas where flammable liquids, vapors, gases or combustible dusts are likely to occur in large quantities, sufficient to cause a fire or explosion.

- Explosion proof (Accredited by CNEx/CQST with EXD II CT6 certification)

- Bullet proof (Resistant to the impact from a normal explosion and short gun bullets)

- Vandal proof (Resistant to the destructiveness of stones, bricks)

- Water proof (Sealed to IP66 and NEMA 4X)

- Corrosion proof (The stainless steel body is long lasting, even when exposed to acid rain and seawater)

- Integration of Day/Night camera, receiver, variable high-speed pan/tilt motor and enclosure

- JM612-V6 series are machined from 8mm~22mm thick Aluminum alloy or 316#Stainless Steel, coupled with its unique sound and solid dome body design, it efficiently prevents from any destructiveness that might threaten in normal use.

- Flat designed optics window from filmed and toughened glass (5mm thick) offers distortion free image and maximum vandal resistant protection for IOP (Integrated Optical Package) camera module

- Unique DIP switch design, provides ease of use

- Motor calibration in manual or auto, guarantee preset and precise running

- Alarm box and water pump system - optional

- IP66/CE/FCC/RoHS compliance

- Support with LeadEx firmware online remote upgrade module

- Optional built-in IP module

- Built-in Sony or Hitachi IOP camera module

- Back light compensation on/off selectable & WDR functions

- 8 Privacy Masking Zone and OSD password protection   (Please see the camera parameters)

- OSD password protection

- User definable 128 target presets, 8 preset tours, video frozen

- Programmable Pattern and auto scan

- User definable power-up action and temperature control

- User definable left and right limitation, proportional Pan speed

- RS-485 communication port, RS-232, RS-422 for optional

- Compatible to Pelco P/D protocol and customized protocol - optional

- Auto / Manual zero calibration

- OSD programming menu, inside temperature and pan/tilt/zoom position

- Surge and non-volatile protection

- Aluminum alloy or #316 stainless steel body: 8mm ~ 22mm

- Filmed and toughened glass: 5mm

- Continuous working temperature：-20°C -- +50°C

- Storage temperature: -40°C -- +60°C

- Net weight: 10KG (Al alloy), 24KG (Stainless Steel)

- Dimension: 370 x 212 mm (see chart)

- Packing Volume: 68 x 46.5 x 32.5 cm

- Input voltage: 18VAC~30VAC/ 18VDC~30VDC

- Maximum Power: 50VA

- Pan/tilt speed: Pan 0.1°~100°/s Tilt: 0.1 ° ~ 80° /s

- Preset speed:  Pan 100° /s  Tilt ：80 ° /s

- Preset accuracy: +/- 0.1° (auto /hand control.)

- Auto scan:      1°-40°/s

- Pan rotation:   360° Tilt rotation: 360°

The JM612-V6 Series are also integrated with the special 5 Proofs design. That is: Bullet proof, Vandal proof, Water proof, Corrosion proof and Explosion proof. Because of its explosion proof features it is very popular in “Hazardous Areas” or an “Explosive Atmosphere” and in the likely/related areas where flammable liquids, vapors, gases or combustible dusts are likely to occur in large quantities, sufficient enough to cause a fire or explosion.

The height of JM612-V6 Series dome body is lower than the JM612-V8 Series that is used in loading vehicles. The housing of the JM612-V6 Series is more spacious than other modules.

It’s own unique omni-seal waterproof and explosion proof design, coupled with it’s sound and solid dome body make it tailor made to be applied in a typical application, this includes: marine transportation, military foundation, perimeter protection, ammunition depot, jails, ports, nuclear facility, Oil refineries, rigs and offshore drilling platform, oil and gas stations, chemical plants, embassies, airports, city surveillance, government, banks and vehicles (off-road vehicles, police cars, military vehicles) etc.

As an option, N2 Nitrogen gas (Maximum pressure within 150Kpa) could be filled into the dome body through a specially designed air vent valve. This could offer further protection to the inner parts, and adapt to the industry and marine related installation, like seaports, ships and chemical plants.

LEADEX JM612-V6 ROBOT SPEED Dome Series could match perfectly with the newly released LeadEx Dual Microwave Detection Unit (DMD Technology). One DMD unit includes 4 dual microwave detectors, each detector covers up to 35m for human detection and 70~100m for vehicle detection at 90 degrees.

In case one detector detects one alarm, the LEADEX JM612-V6 ROBOT SPEED Series could automatically turn to this zone and active the auto-tracking function to track the moving objects. A total area of 360 degrees is under protection.

The traditional video based motion detection system becomes very weak and performs poorly in the dark, rainy or windy weather conditions. While LEADEX DMD technology is immune to leaves falling, small birds flying and tree movement/swaying. It combined with JM612-V6 Series offers a more professional and safer area of protection.

The most outstanding advantages of these dual microwave detectors, is that it is totally effective to the interfering of wind, rain, fog or any drifting small objects. So the LEADEX JM612-V6 ROBOT SPEED Dome Series with motion detection device are designed to fit perfectly while working in the darkest of environment with rarely a false alarm.

.

| Camera | 18X Day/Night (Sony FCB-EX490) | 26X Day/Night (Sony FCB-EX490) | 36X Day/Night (Sony FCB-EX1010) |
| --- | --- | --- | --- |
| Material |  |  |  |
| Aluminum Alloy | JM612A-V6-18 | JM612A-V6-26 | JM612A-V6-36 |
| 316L# Stainless Steel | JM612S-V6-18 | JM612S-V6-26 | JM612S-V6-36 |

EXPLOSION-PROOF CERTIFICATE OF CONFORMITY

For JM612 ROBOT SPEED DOME

### GENERAL INFORMATION:

LeadEx JM612 SERIES Robot Speed Dome Camera (also called Solid Speed Dome) is designed and proved to be explosion proof, accredited by CNEx/CQST (China National Quality Supervision and Test Center for explosion Protected Electrical Products), the legal professional testing and certification body in Explosion safety test, verification and approval.

CNEX/CQST is an IECEx (International Electrotechnical Commission Scheme for certification to standards for Explosive Atmospheres) testing laboratory in accordance with the IECEx scheme rules and procedures. And the lab is also authorized by Department of Energy of USA for NVLAP, and accredited by CNAL (China National Accreditation Board for Laboratories) and CCS (China Classification Society).

CQST signed the mutual acceptance and/or mutual understanding agreement with the laboratories such as UL (USA), PTB (Germany), NEMKO (Norway), FMRC (USA), TESTSAFE (Australia), LCIE (France), CCVE (Russia), CSA (Canada), BASEEFA (UK) and so on. (Agreement photocopies are available on request).

### EXPLOSION TESTINGS WITH COMBUSTIBLE GAS:

The Robot Speed Dome Camera experienced explosion testing by combustible gas (METHAME and HYDROGEN) in different pressure conditions, with explosion from both inside and outside.

(Above Photo: LeadEx Robot Dome is undergoing explosion proof testing)

### STANDARDS & EX MARKING:

Standards as below:

IEC60079-0:2004 - Electrical apparatus for explosive gas atmospheres – Part 0: General requirements

IEC60079-1:2003 - Electrical apparatus for explosive gas atmospheres – Part 1: Flameproof enclosure “d”

GB3836.1-2000 - Electrical apparatus for explosive gas atmospheres – Part 0: General requirements

GB3836.2-2000 - Electrical apparatus for explosive gas atmospheres – Part 1: Flameproof enclosure “d”

Q/LDX001-2007- Enterprise standards for electrical apparatus for explosive gas atmospheres

EN50014 ff - Electrical apparatus for explosive gas atmospheres (Europe Union)

Marking: Exd II CT6

(C15888, C15889, C15890) Exd II CT6.
Approved by CNEx/CQST (in China) Class I Division 1, Groups B, C, and D.
Certified by EC-TYPE EXAMINATION, KEMA 04ATEX2045X, II 2G EExd II CT6, II2D T180 degree centigrade.

CERTIFICATE OF ACCEPTANCE- IECEx Testing Laboratory:

IECEx Member Bodies are listed below:

Australia, Canada, China, Czech Republic, Denmark, Finland, France, Germany, Hungary, India, Italy, Japan, Korea, Netherlands, New Zealand, Norway, Republic of Serbia, Romania, Russia, Singapore, Slovenia, South Africa, Sweden, Switzerland, UK, USA

### PHOTOCOPIES OF MUTUAL ACCEPTANCE AGREEMENTS:

### PHOTOCOPIES OF JM612 CERTIFICATE OF CONFORMITY:

### OTHER CERTIFICATION:

IP66 Test Report                                      CE