PowerView Plus Fog Penetrate PTZ Camera (PVP)

The PowerView Plus series is a precise pan/tilt/zoom camera system with built-in mega-pixel big lens, special camera, and infra-red laser illumination, which has excellent performances at daytime and night, even on a foggy or rainy day.

The built-in zoom lens is designed to match the high sensitive day / night camera and IR Laser illumination, and to minimize the difference between the focus panel with a visible radiation and also with a near-infrared radiation.

The state-of-the-art design of pan/tilt system offers not only flexible pan and tilt rotation, but also delivers an accurate user controllable interface; which allows users to operate the system in “micro-step” control. The laser illuminator working at 808nm freq has a total 8000mW optical output, which offers a super powerful light source for the camera in night working applications.

With the above outstanding technologies, the PowerView Plus is a long range camera system, capable to

see targets 3~6 km away, and even objects in a dark night and those behind the fog, rain and smog.

- Integration of Fog Penetrate camera, Mega Pixel Lens, adjustable IR Laser, receiver, variable high-speed pan/tilt motor and enclosure

- PVP series are machined from the mixed A3 armor plate, coupled with its unique sound and solid dome body design, efficiently prevents destruction and threats of misuse (in practical use).

- Flat designed optics window from filmed and toughened glass (5mm thick) offers distortion free image and maximum vandal resistant protection for IOP (Integrated Optical Package) camera module

- Unique DIP switch design, offers the operator an easy-to-use window

- Motor calibration in manual or auto guarantee preset precise continuous running

- Alarm box and water pump system - optional

- IP65/CE/FCC/RoHS compliance

- Support with LeadEx firmware online remote upgrade module

- Optional built-in IP Module

- Built-in Fog Penetrate camera (520TVL, 0.01Lux sensitivity)

- Lens Option: 10~320mm, 20~640mm,15~750mm, 30~1500mm - optional

- Motorized Focus and Zoom

- Built-in the 808nm long distance Laser-IR illuminator with light power 2000mw

- Laser ON/OFF by manual (or auto control – optional)

- OSD password protection

- User definable 128 target presets, 8 preset tours, video frozen

- Programmable Pattern & auto scan

- User definable power-up action and temperature control

- User definable left and right limitation, proportional pan speed

- RS-485 communication port, RS-232, RS-422 - optional

- Compatible to Pelco P/D protocol and customized protocol - optional

- Auto / Manual zero calibration

- OSD programming menu, inside temperature and pan/tilt/zoom position

- Surge & non-volatile protection

- Machined from the mixed A3 armor plate

- Filmed and toughened glass: 5mm

- Continues working temperature：-20°C -- +50°C

- Storage temperature: -40°C -- +60°C

- Input voltage: AC24V, 50HZ

- Maximum Power: 72VA (Laser ON)

- Pan/tilt speed: Pan 0.09°~80°/s  Tilt: 0.09 ° ~ 25° /s

- Preset speed:  Pan 80° /s      Tilt: 25 ° /s

- Preset accuracy: +/- 0.03° (auto /hand control)

- Auto scan:      1°-40°/s

- Pan rotation:   360° Tilt rotation:    -74°~+45°

- Laser electric current: Average 245mA

- Laser working voltage: Average 2050 mV

- Slope efficiency: Average 1.20

- Laser wave length: 808nm （Please see the Laser spectrogram）

- Electric working electric current: 2000mA

- Electric light efficiency: 2000mW

- Laser Angle: 1° ~8°

Laser electric current- Power Consumption Specification chart

| Iris Characteristics | a) Control | Auto or manual remote |
| --- | --- | --- |
|  | b) Rating Voltage | +12V DC (+9V to +15V) |
|  | c) Input Signal | Composite video signal (1V(p-p)) or video signal (0.7V(p-p)) |
|  | d) Input Impedance | 10 KΩ (TYP) |
|  | e) Level Control Range | See fig. A |
|  | f) Accuracy | ±3.5% (at 0.5V APL *) |
|  | g) Current Consumption | Operating current 45mA (MAX) Idling current 25mA (TYP) |
|  | h) Response Time | Approx. 2s/full travel |
|  | i) Function | Level remote |
| Zoom Characteristics | a) Control | Motor drive |
|  | b) Rating Voltage | 6V/12V/±6V/±12V DC (Switchable) |
|  | c) Current consumption | Operating current 30mA (TYP) 90mA (MAX) |
|  | d) Operating Time | Approx. 8s/full travel |
|  | e) Potentiometer | 10 kΩ 0.5W |
| Focus Characteristics | a) Control | Motor drive |
|  | b) Rating Voltage | 6V/12V/±6V/±12V DC (Switchable) |
|  | c) Current consumption | Operating current 30mA (TYP) 90mA (MAX) |
|  | d) Operating Time | Approx. 8s/full travel |
|  | e) Potentiometer | 10 kΩ 0.5W |

| Application |  | For 1/2" format day/night camera |
| --- | --- | --- |
| focal length |  | 10mm~320mm |
| zoom ratio |  | 32X |
| Maximum relative aperture |  | 1:25 |
| Iris range |  | F2.5-T1500 (Equivalent to F1500) |
| Image size |  | φ8mm (6.4mm X 4.8mm) |
| back focal length |  | 22.7mm (In air) |
| flange focal length |  | 17.526mm (In air) |
| Focus range |  | ∞ ~ 3mm (From front of lens) |
| Shift of front lens |  | 6.85mm |
| Field angle | Horizontal | Wide 35°29′ Tele 1°09′ |
|  | Vertical | Wide 26°59′ Tele 0°52′ |
|  | Diagonal | Wide 43°36′ Tele 1°26′ |
| Field of view at M.O.D. | Horizontal | Wide 1746mm Tele 57mm |
|  | Vertical | Wide 1310mm Tele 43mm |
| Clear aperture | Front | φ76.0mm |
|  | Rear | φ12.0mm |
| Exit pupil position |  | -53mm (from image plane) |
| Lens Dimension |  | 134*114*224.8mm |
| Lens weight |  | 2.5kg |

| Model Number | Description |
| --- | --- |
| PVP-320 | Built-in 10~320mm Long Range Fog Penetrate Lens |
| PVP-640 | Built-in 20~640mm Long Range Fog Penetrate Lens |
| PVP-750 | Built-in 15~750mm Long Range Fog Penetrate Lens |
| PVP-1500 | Built-in 30~1500mm Long Range Fog Penetrate Lens |