LeadEx Speed Dome Series (LDX-D)

- Integration of  digital camera, lens, receiver, variable high-speed pan/tilt motor and enclosure

- Dome housing: 5.9-inch Aluminum Alloy

- Dome drive: ABS Plastic and Aluminum

- Dome cover: clear or smoked color acrylic, (Polycarbonate Vandal proof material is optional)

- Surge & non-volatile protection

- DIP switch setup for protocol, baud rate and address ID

- Motor calibration in manual or auto guarantee preset precise and continuous running

- IP66/CE/FCC/RoHS compliance

- Support with LeadEx firmware online remote upgrade module

- Optional built-in IP module

- Built-in Sony or Hitachi IOP camera module

- Back light compensation on/off selectable & WDR functions

- 3 selectable white balance: auto/on/off, Red-Blue, Auto focus and Iris

- Auto tracking and motion detection function for optional(Hitachi Camera Module)

- 8 Privacy Masking Zone and OSD password protection   (Please see the camera parameters)

- OSD password protection

- User definable 128 target presets, 8 preset tours, Preset frozen

- Programmable Pattern & Auto scan

- User definable power-up action and temperature control

- User definable left and right limitation, proportional pan speed

- RS-485 communication port, (RS-232, RS-422 - optional)

- Compatible to Pelco (P/D protocol and customized protocol – optional)

- Built-in 8 Alarm inputs; 2 Alarm outputs

- Auto / Manual zero calibration

- OSD programming menu, inside temperature and pan/tilt/zoom position

- Surge & non-volatile protection

- Privacy Mask function, 8 privacy zone

- Aluminum Alloy housing, ABS Plastic dome drive

- Dome cover: 5.9 inch sealed fixed acrylic bubble

- Continues working temperature: -10°C -- +50°C

- Storage temperature: -20°C -- +85°C

- Package dimension (LxWxH): 66x34x29CM

- Gross weight (with adapter): 6.5KG(in-ceiling), 7KG(in-door pendant), 7.5KG(outdoor pendant)

- Adapter Input voltage: AC150V~ AC240V, 50HZ

- Output voltage to the dome: AC16V~AC26V, 50HZ

- Maximum Power: 30W

- Variable high-speed pan/tilt: 0.05°- 250°/S pan  0.05°- 200°/S tilt

- 360° Continuous Pan Rotation, Automatic 180° flip

- Preset Speed: 250°/S pan, 200°/S tilt

- Preset accuracy: +/- 0.03° (auto /hand control.)

- Auto scan:      1°-40°/s

- Pan rotation:   360°  Tilt rotation:   +2° ~-92°

- 1 presets tour available to call 1 to 8 presets in sequence*

The LDX-DC Integrated Speed Dome Camera is the integration of Day/Night camera, lens, multi-protocol receiver, variable high-speed pan/tilt and dome enclosure. A complete speed dome is composed of dome housing, a plastic (clear or smoked color) lower dome (bubble) and a dome drive with a built-in camera and lens, the connection PCB unit is included in the dome housing and the system mother board is inside the dome driver.

The system is noted for its high acceleration rate with smooth, steady motion and flexible presets programming and setup. The dome driver features an Integrated Optics Package camera and a mechanical /electrical quick disconnect system, making installation quick and easy.

The Speed Dome System is available as either an in-ceiling or pendant mount (indoor or outdoor) model. The in-ceiling system may be installed in either suspended or hard ceilings. The pendant model mounts directly to any recommended mount, flush to a ceiling or to NPT female threaded pipe. All outdoor pendant models are environmentally sealed to a rating of NEMA 4X and IP66 and include a sunshield, heater and fan. (See housing pictures of indoor in-ceiling mount, indoor pendent mount and outdoor pendent mount.)

The dome is capable of 360° continuous pan rotation and 92° tilt rotation with auto-flip function. UP 128 target presets could be setup to see specific target scenes automatically after receiving a preset call command or alarm. Frozen preset call is optional to avoid un-useful fast moving scene during preset call up period, thus only presets are displayed one by one on the screen.

The sequence tour is available to call up to 8 presets in sequence with user programmable dwell time. A user programmable home position will ensure that the dome will turn back to important presets after 2 to 255 seconds of un-activated time. Built-in 8 alarm inputs will call #1-8 presets automatically in case of alarm and trigger the 2 auxiliary outputs.

The pattern, which is also called PTZ learning in some countries, enables the user to control the pan/tilt zoom and call presets within 2 hours, and the dome will learn and save the user’s operation. The user could call up the pattern and let the dome run automatically, just like the operator is controlling the dome.

The On-Screen-Display menu makes it fast and easy for the detailed system programming such as alarm joint-action-control setup, and camera parameter adjustment and so on.

DIP setup for protocol, LDX-DC series will adapt to the controller’s protocol (Pelco-P or –D) and baud rate (2400/4800/9600). Privacy Mask function, The user can set 8 privacy zone.

LDX-D Dome Series can match perfectly with the newly released LeadEx Dual Microwave Detection Unit (DMD Technology). One DMD unit includes 4 dual microwave detectors; each detector covers up to 35m for human detection and 70~100m for vehicle detection at 90 degrees.

In case one alarm is detected by one detector, the LDX-D Series could automatically turn to this zone and activate the auto-tracking function to track the moving objects. Total 360 degree area is under protection.

The traditional video based motion detection becomes very weak and had bad performance in dark night, rainy or windy weather conditions.  While LEADEX DMD technology sorts out all the troubles, and is also immune from leaves falling, small birds flying and trees swaying. It combines with LDX-D Series to offer more professional and safer protection.

The most outstanding advantages of the dual microwave detectors is that it is totally effective to the interfering of wind, rain, fog or any drift small objects. So the LDX-D Speed Dome Series with motion detection device are designed to fit to working in most darkness environment with rare false alarm.

LDX-D Speed Dome System is available as either an in-ceiling or pendant mount (indoor or outdoor) model. Please see the following chart.

- Indoor in-ceiling: may be installed in either suspended or hard ceilings. Do not need the bracket.

- Indoor pendant model mount: can be directly affixed to any recommended mount, flush to a ceiling, or to NPT female threaded pipe.

- Outdoor pendant models: they are environmentally sealed to a rating of NEMA 4X and IP66 and include a sunshield, heater and fan.

| BRAND | Camera Model | Products Model |
| --- | --- | --- |
| HITACHI | VK-S214 | LDX-D22C |
|  | VK-S274 | LDX-D22L |
|  | VK-S858 | LDX-D23S |
|  | VK-S654 | LDX-D35S |

| BRAND | Camera Model | Products Model |
| --- | --- | --- |
| SONY | FCB-EX45 | LDX-D18C |
|  | FCB-EX480/490 | LDX-D-18S |
|  | FCB-EX980/990 | LDX-D26S |
|  | FCB-1000/1010 | LDX-D36S |

Note: I=Indoor In-Ceiling Mount D=Indoor Pendant Mount P=Outdoor Pendant Mount

Such as: LDX-D-18S -P means 18X  day/night outdoor pendant mount

# Text boxes

LDX-D series high speed dome is the integration of Day/Night camera, lens, receiver and variable high speed pan/tilt motor.

The housing contains aluminum alloy material which is high temperature and corrosion resistant, designed to be waterproof (IP66 standard). The cover consists of an imported polycarbonate material that can keep the image distortion free. To make the dome body vandal proof , the PVC material is an option.

LDX-D series high speed dome mainly applies to the City Surveillance, Schools, Hospitals and Road Surveillance, Bank and Airport etc.