Video Analytics Module

VAM—Video Analytics Module from LeadEx is an enhance rule-driven detection surveillance device which effectively automates the time critical task of monitoring video and detecting events thus providing a high probability of detection while maintaining a remarkably low false alarm rate.

Product Features

|  | Intrusion Detection Automatically detects prohibited movement scenarios Regional Entrance detection Tripwire detection Fence trespassing detection |
| --- | --- |
|  | Stopped Vehicle Detection Detects vehicles stopped in a controlled area Immediate or delayed alarm notification |
|  | Unattended Baggage Detection Alarms when an item is deposited in a controlled area Ignores items attended by a nearby person Detects disguised objects |
|  | Object Removal Detection Detects the removal of stationary objects Delayed alarm notification for object retrieval |
|  | Object Counter Provides a counting function in the specific area or region, and summary report available at certain time frames. |
|  | Autonomous PTZ Tracking – (Optional) Independently tracks and visually relays moving targets Self-directed vision-guided tracking PTZ synchronized hand-off |
|  | Loitering Detection Detects when a person remains in an area for a prolonged period of time Adjustable alert time for different scenarios |
|  | Camera Tampering Detection Provides an alarm when camera operation is disrupted due to No video signal Bad video signal Camera position shift Low Visibility |

Performance

• High probability of detection while maintaining a remarkably low rate of false alarms

• Detects intruders under harsh weather conditions, low visibility, and poor lighting

• Superior non-flat detection sees objects in 3D-scape and at great distances for reliable detection

• Supports pre-alarm recording for capturing the moments before an alarm

Optimized Automatically

All modules use a variety of built-in processes that automatically compensate and adjust to avoid false alarms and assure best image quality for optimized detection:

• Background learning for differentiating trivial movements from those of interest

• Automatic adjustments to optimize detection for dynamic lighting changes whether rapid or gradual

• Automatic image quality adjustments to increase image detail for optimized detection

• On-event-management of video stream resolution and frames per second

Customized Selection

- Superior non-flat detection, judges real-life size equivalency, speed, and distance in a 3D-scape measurement model, which is based on following parameters as:

>> Camera installation Angle

>> Camera installation Height

>> Target Size based on human as reference substance

- Free-drawn regions of interest provide greater control of where detection is to take place for best fit detection based on the uniqueness of an individual scene.

Alert Automation

  - Mechanical: VAM includes an event engine for defining response to alarms and events that allow controlling and turning on and off mechanical devices via dry contacts.

  - Email / SMS: VAM support sending any event and alarm message with snapshot to designated email account or any SMS to mobile phone device.

Built-in Video Server

  - H.264/ MPEG4/ MJPEG

  - Support duel streaming technology

  - Individual setting for difference stream

  - Built-in SD Card for local recording and snapshot

Support PTZ operation (Pelco-D/E)

  - Pan/ Tilt

  - Zoom

Product Technical Specification

| Video |
| --- |
| Input | 1 Channel (CVBS, ITU-R BT.656) |
| Output | 1 Channel (BNC Connector) |
| Encoder Standard | H.264, MPEG4, MJPEG |
| Duel Streaming | Support with H.264, MPEG4, MJPEG |
| Resolution | D1, 2CIF, CIF, QCIF |
| Frame Rate Per Second | 25/30 FPS @D1 |
| Interlace | Support (DSP) |
| VMD | Support (DSP) |
| Burnt-in Text (Digital) | Support (DSP) |
| Audio |
| Input | 1 Channel |
| Output | 1 Channel |
| Encoder Standard | G.711 |
| I/O |
| Alarm Input | N/A |
| Alarm Output | 8 |
| RS-485/422 | Optional |
| RS-232C | N/A |
| Network | 10 / 100 Base-T |
| Network Protocol | TCP/IP, UDP/IP, HTTP, RTSP, RTCP, RTP/UDP, RTP/TCP, SNTP, mDNS, UPnP, SMTP, SOCK, IGMP, DHCP, FTP, DDNS, PPPoE, SSL v2/v3, IEEE 802.1X, SNMP, SSH, and IPv6 |
| USB 2.0 | Support (Video Back-up) |
| SD Card Memory | Support (Video Storage) Up to 32GB |
| Power Requirement |
| Input Voltage | 12V DC |
| Power Consumption | 210 mA @ +12V |
| Operation Temperature |
| Operation Temperature | 0 °C ~ 60°C (32 °F ~ 140°F) |
| Operation Humility | Up to 85% RH (Non-condensing) |
| Physical Parameter |
| Dimension | 113.5(W)×27.3(H)×63.9(D) mm |
| Weight (Approx) | 80g |

Optional Built-in Modules for LeadEx V6, Laser ROBO, Thermal ROBO, PVP Thermal models

# Text boxes

Video IN

Video OUT

EXT1

EXT2

Audio IN

USB Slot

SD Card Storage

RESET

Audio OUT

LAN

Power Input